## Slide 1
Flip-Flops and Latches
© 2014 Project Lead The Way, Inc.
Digital Electronics

## Slide 2: Flip-Flops & Latches
This presentation will
Review sequential logic and the flip-flop.
Introduce the D flip-flop and provide an excitation table and a sample timing analysis.
Introduce the J/K flip-flop and provide an excitation table and a sample timing analysis.
Review flip-flop clock parameters.
Introduce the transparent D-latch.
Discuss flip-flop asynchronous inputs.
Notes: Introductory Slide / Overview of Presentation

## Slide 3: Sequential Logic & The Flip-Flop
Combinational
Logic Gates
.
.
Inputs
Outputs
Memory Elements
(Flip-Flops)
.
.
Clock
Notes: Definition of sequential logic. Sequential logic can have one or more, inputs and one or more outputs. However, the outputs are a function of both the present value of the inputs and also the previous output values. Thus, sequential logic requires memory to store these previous outputs values.

## Slide 4: D Flip-Flop: Excitation Table
CLK
D
Q
D | CLK |  | 
0 |  | 0 | 1
1 |  | 1 | 0
 : Rising Edge of Clock |  |  | 
Notes: Schematic symbol and excitation table for the D flip-flop.

## Slide 5: D Flip-Flop: Example Timing
Q |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
D |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
CLK |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Q=D=1
Q=D=1
Q=D=0
Q=D=1
No Change
Q=D=0
No Change
Q=D=0
No Change
Q=D=0
Notes: Timing diagram example for a D flip-flop.

## Slide 6: J/K Flip-Flop: Excitation Table
J | K | CLK |  | 
0 | 0 |  |  | No Change
0 | 1 |  | 0 | Clear
1 | 0 |  | 1 | Set
1 | 1 |  |  | Toggle
 : Rising Edge of Clock |  |  |  | 
K
J
Q
CLK
Notes: Schematic symbol and excitation table for the J/K flip-flop.

## Slide 7: J/K Flip-Flop: Example Timing
Q |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
J |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
K |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
CLK |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
SET
CLEAR
TOGGLE
NO
CHANGE
TOGGLE
NO
CHANGE
SET
Notes: Timing diagram example for a J/K flip-flop.

## Slide 8: Clock Edges
1 0 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
1 0 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Positive Edge Transition
Negative Edge Transition
Rising Edge
Falling Edge

## Slide 9: POS & NEG Edge Triggered D
CLK
D
Q
D | CLK |  | 
0 |  | 0 | 1
1 |  | 1 | 0
 : Rising Edge of Clock |  |  | 
D | CLK |  | 
0 |  | 0 | 1
1 |  | 1 | 0
 : Falling Edge of Clock |  |  | 
CLK
D
Q
Positive Edge Trigger
Negative Edge Trigger
Notes: Schematic symbol and excitation table for the positive edge triggered and negative edge triggered D flip-flops

## Slide 10: POS & NEG Edge Triggered J/K
Positive Edge Trigger
Negative Edge Trigger
K
J
Q
CLK
K
J
Q
CLK
J | K | CLK | 
0 | 0 |  | 
0 | 1 |  | 0
1 | 0 |  | 1
1 | 1 |  | 
 : Rising Edge of Clock |  |  | 
J | K | CLK | 
0 | 0 |  | 
0 | 1 |  | 0
1 | 0 |  | 1
1 | 1 |  | 
 : Falling Edge of Clock |  |  | 
Notes: Schematic symbol and excitation table for the positive edge triggered and negative edge triggered J/K flip-flops

## Slide 11: Flip-Flop Timing
Data Input (D,J, or K) | 1 0 |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  |  | tS Setup Time |  |  |  |  |  |  |  |  | tH Hold Time |  |  | 
Positive Edge Clock | 1 0 |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Setup Time (tS): The time interval before the active transition of the clock signal during which the data input (D, J, or K) must be maintained.
Hold Time (tH): The time interval after the active transition of the clock signal during which the data input (D, J, or K) must be maintained.
Notes: Definition of the Setup & Hold Time timing parameters for a flip-flop.

## Slide 12: Asynchronous Inputs
PR PRESET | CLR CLEAR | CLK CLOCK | D DATA |  |  | 
1 | 1 |  | 0 | 0 | 1 | 
1 | 1 |  | 1 | 1 | 0 | 
0 | 1 | X | X | 1 | 0 | Asynchronous Preset
1 | 0 | X | X | 0 | 1 | Asynchronous Clear
0 | 0 | X | X | 1 | 1 | ILLEGAL CONDITION
CLK
D
Q
PR
CLR
Asynchronous inputs (Preset & Clear) are used to override the clock/data inputs and force the outputs to a predefined state.
The Preset (PR) input forces the output to:
The Clear (CLR) input forces the output to:
Notes: Definition for the PR (preset) and CLR (clear) Asynchronous input for a D flip-flop.

## Slide 13: D Flip-Flop: PR & CLR Timing
Q |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
PR |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
CLR |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
D |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
CLK |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Q=1
Preset
Q=D=0
Clocked
Q=D=0
Clocked
Q=1
Preset
Q=D=0
Clocked
Q=0
Clear
Q=D=1
Clocked
Q=D=1
Clocked
Q=D=1
Clocked
Notes: Time diagram showing the effects of the synchronous inputs (D & CLK) and asynchronous inputs (PR & CLR).

## Slide 14: Transparent D-Latch
EN
D
Q
EN | D |  | 
0 | X |  | 
1 | 0 | 0 | 1
1 | 1 | 1 | 0
EN: Enable
Notes: Schematic symbol and excitation table for the D latch.

## Slide 15: Transparent D-Latch: Example Timing
Q |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
D |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
EN |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
“Latched”
Q=0
“Latched”
Q=1
“Latched”
Q=0
“Transparent”
Q=D
“Transparent”
Q=D
“Transparent”
Q=D
Notes: Time diagram example for a transparent D-latch.

## Slide 16: Flip-Flop Vs. Latch
The primary difference between a D flip-flop and D latch is the EN/CLOCK input.
The flip-flop’s CLOCK input is edge sensitive, meaning the flip-flop’s output changes on the edge (rising or falling) of the CLOCK input.
The latch’s EN input is level sensitive, meaning the latch’s output changes on the level (high or low) of the EN input.
Notes: This slide details the primary difference between the often confused D flip-flop and D latch.

## Slide 17: Flip-Flops & Latches
74LS74
Dual Positive-Edge-Triggered D Flip-Flops with Preset, Clear, and Complementary Outputs
74LS76
Dual Negative-Edge-Triggered J-K Flip-Flops with Preset, Clear, and Complementary Outputs
74LS75
Quad Latch
Notes: Summary of the two flip-flops and one latch that we will be using in this course.

## Slide 18: 74LS74: D Flip-Flop
Notes: Datasheet excerpts for a 74LS74 D flip-flop.

## Slide 19: 74LS76: J/K Flip-Flop
Notes: Datasheet excerpts for a 74LS76 J/K flip-flop.

## Slide 20: 74LS75: D Latch
Notes: Datasheet excerpts for a 74LS75 D latch.